## Slide 1
From NEMO to KM3NeT-Italy
Carlo Alessandro Nicolau
on behalf of the
KM3NeT-Italy Collaboration

## Slide 2
The NEMO Phase 2 project
  The Capo Passero Site
  The NEMO Phase 2 prototype tower
The KM3NeT-Italy project
  Communication architecture
  New electronics
Conclusions

## Slide 3
BT
Capo Passero site Infrastructure
And
the NEMO Phase 2 Tower
On-shore
Off-shore
20 x opt. fib.
10 kV
~100 km
NEMO Phase 2 Tower
375VDC
2 x opt. fib.
MVC
&
Opt. splitter
Operating since Apr. 2013
Shore Laboratory in Capo Passero harbour
Control Room
Guest House
DAQ
Power Feeding Equipment

## Slide 4
NEMO Phase 2 Tower
Main characteristics:
8 “Floors”:
  8 m in length
  40 m vertical distance
8 x 4 Optical Modules:
  PMT signal acquisition
8 x 2 Hydrophones:
  Continuous sampling at 24 bit / 192 kHz
Calibration sensors
  Laser beacon
  LED-beacon, TIM-CAL
Oceanographic Sensors:
  Conductivity/Temperature/Depth
  Transmissivity
  Current speed meter
Fully synchronous communication protocol:
  Each device of the apparatus is “timestamp-aware” by design
  Compatible with DWDM standard
  Reduced number of optical fibers
All data to shore

## Slide 5
NEMO Phase 2 Point to point link
Floor Control Module
NEXT FLOOR
PREV. FLOOR
TRANSCEIVER DWDM
RX
TX
DROP
ADD
on-shore
lab
EFCM

## Slide 6
NEMO Phase 2 Floor
SCI
AcouDAQ
NEXT FLOOR
PREV. FLOOR
375VDC
RS-485
12V
5.5V
4.2V
CPS
FCM
Hydrophones
CTD / CSTAR / DCS
TimCTRL
RS-232
ADD/DROP
backbone
backbone
CPS

## Slide 7
NEMO Phase 2 Optical Module Electronics
Front End Module
LED
Pulser
LED-Beacon
Controller
HV
PSU
RFID Reader
Ext. Sensor
TIM-CAL
reach upper
floor OMs
Control (I2C)
Trigger
Power
LV RS232
Power
Control
Monitor
CLOCK
DIN / VCC
DOUT / GND
TO/ FROM FCM

## Slide 8
NEMO Phase 2 Timing distribution
GPS receiver
Ethernet Floor
Control Module
On-Shore
To other EFCMs
Timing distribution board
FCM
Off-Shore
Absolute Time Information
Clock / Data / Timing
Embedded in a single bitstream, carried by a single DWDM wavelength

## Slide 9
NEMO Phase 2 Data distribution
Control Room
TriDAS
ETHERNET
Slow Control
AES3
Power
Control
Audio
DWDM MUX
Media
converter

## Slide 10
Phase 2
Tower
KM3Net-Italy project layout
KM3
Net-IT
T#6
20 x opt. fib.
6kV
Junction
Box
Main E/O Cable
KM3
Net-IT
T#5
KM3
Net-IT
T#8
KM3
Net-IT
T#2
KM3
Net-IT
T#1
KM3
Net-IT
T#4
KM3
Net-IT
T#3
KM3
Net-IT
T#7
375VDC
2 x opt. fib.
375VDC
2 x opt. fib.

## Slide 11
Junction Box

## Slide 12
KM3Net-Italy tower layout
Tower base
Floor #1
Floor #2
Floor #13
Floor #14
E/O Cable
Junction
Box
14 Floors + Base Tower
6 OMs per floor
FCM
H
H
BT
FCM
FCM
FCM
Star connection topology instead of daisy-chain
Daisy-chain topology implies
power loss due to connectors
2
375 V

## Slide 13
Base Tower
Laser
beacon
Digital
hydrophone

## Slide 14
Slow Control
Acoustic DAQ
Floor Control Module
OM #0
RS232 Port
Compass (+3.3V)
RS232 Port
Ext Instrument
(Isolated, +12V)
2 x Digital AES3
Hydrophone
Spare RS232 Port
(Isolated, +12V)
OM #1
OM #2
OM #3
OM #4
OM #5
375 V
Power Connectors
1.2 V, 3.3 V, 5 V, 12 V
(V & I Measurement)
Floor Control Module
Power Supply System
KM3NeT-IT Floor electronics
TimCTRL
CPS

## Slide 15
KM3NeT-IT Floor electronics
NEMO Phase 2
KM3NeT-IT
Dissipative linear voltage regulators
(12 V, 5 V, 3.3 V, 2.5 V, 1.2)
Lower power consumption
From 7.5 W
To ~3 W
Active low noise DC/DC
5 different boards
2 boards
Simplified integration, lower cost, simplified debug complexity
7 processing units
3 architectures
(Xilinx FPGA, Microchip PIC,
Freescale DSP)
1 processing unit
1 architecture
(Xilinx FPGA w/ uBlaze MCU)
Easier code maintainance
From VHDL / DSPASM / C
To VHDL / C++
Floor Control Module
Power Supply System
Xilinx Spartan 6 FPGA
Fixed latency transceiver onboard (up to 2.5Gbps)
2 opto-isolated serial port
1 user serial port
2 x AES3 stereo inputs
6 x OM interface
Power requirement (FCM): ~2 W
Safe reconfiguration from remote
DC/DC (375 V -> 5 V -> 1.2, 2.5, 3.3, 12 V)
Voltage and current measure

## Slide 16
KM3NeT-IT Optical Module
FEM
LED beacon
controller
TIM-CAL
HV
PSU
Front End Module
CLOCK
DIN / VCC
DOUT / GND
TO/ FROM FCM
USER CONN
(Power, AIN, GPIO, I2C, RS232, ...)
GATE In
PMT signal
HVPSU
Power
Control
Feedback
LED Beacon
Power
Trigger

## Slide 17
KM3NeT-IT Front End Module
Front End Module
NEMO Phase 2
KM3NeT-IT
2 Processing units
2 Architectures
(Xilinx FPGA, Freescale DSP)
1 processing unit
1 architecture (same as FCM)
Easier code maintainance
From VHDL / DSPASM
To VHDL / C++
Xilinx Spartan 6 FPGA
Signal sampling:
  single differential 200 MHz 14 bit ADC
  Programmable threshold for Zero-skipping
  8 bit compression on spe signals
  2 kSample FIFO
Analog conditioning:
  Linear analog differential filtering
  ADCs pedestal adjustment
PMT HV management
20 Mbps link to FCM (8b/10b)
Temperature & Humidity sensor
Power requirement: 0.2A @ 5V
Safe reconfiguration from remote (up to three images)
Dissipative linear voltage regulators
Low noise DC/DC
Reduced power consumption
From ~2 W / OM
To ~1 W / OM
2 x 8 bit ADC, non-linear compression
Single 14 bit ADC, linear
Simplified elaboration
No need to “decompress” signals
Simplified calibration process
No need to calibrate each single FEM at different temperatures

## Slide 18
KM3NeT-IT On-shore data distribution
Per tower
DWDM MUX
15 EFCM per Tower
TriDAS
Slow Control
Power
Control
Audio
Ethernet only

## Slide 19
KM3NeT-IT On-shore data distribution – 8 towers
DWDM MUX
15 EFCM (T1)
15 EFCM (T2)
15 EFCM (T8)
120 EFCM
...feasible, but...

## Slide 20
Data rate estimation
1 spe  70 ns  14 samples (8 bit)
Timestamp info
16 bytes per spe hit
+
~1 MB/s per OM
~10 Mbps per OM
~50 kHz spe background rate
x
+
Hydrophones (24 Mbps per floor)
x 2 (safety margin) x 6 OMs
+
Slow control (6 Mbps per floor)
~150 Mbps per floor
15 floors
x
~2.2 Gbps
Per tower
Not a huge data-rate nowadays...

## Slide 21
KM3NeT-IT On-shore data distribution
R&D with APE - INFN Roma1 group
8 x SFP
Can serve half a tower
(~1.1 Gbps)
PCI-express
More than one tower per CPU node
Simplified architecture and maintenance
Possible use of GPU for triggering algorithms
Current R&D status:
Preliminary tests have been performed
Xilinx / Altera communication test at 2.5 Gbps
Next step : fixed latency tests

## Slide 22
Conclusions
The NEMO Phase 2 prototype tower was successfully deployed on late March 2013 and is currently taking data
Preliminary evaluation of acquired data is in progress
The Capo Passero site confirms expectations
The KM3NeT-Italy project is in the production stage
We expect to see the first tower deployed during 2014

## Slide 23
BACKUP SLIDES

## Slide 24
to lower floor
Add
Add
Add
Drop
Drop
Drop
Transceiver
TX
RX
Transceiver
TX
RX
Transceiver
TX
RX
from lower floor
Floor #(n-1)
Floor #n
Floor #(n+1)
to upper floor
from upper floor

## Slide 25
TOWER BASE
E
MANIFOLD
10 m
1
2
.. .
JUNCTION BOX
E
O
O
10 m
10 m
13
14
10 m
FLOOR POD 1
FLOOR POD 14
E
O
ELECTRONICS POD
POWER POD
PHOTONICS POD
E O
E O
E O
E O
E O
E O
Tower Base

## Slide 26
375 V INPUT
from JB
28
2
1
MANIFOLD IBRIDO
E
2
E-O
E-O
13
14
E-O
E-O
O
OPTICAL
FIBERS
375 V
S 1
V
375 V OUTPUT 14
PSS
375V / LV
S 14
PSS
PSS
mC + ADC
FCM
2X8
2
2
2
2
V
T
P
H2O
H2O
H2O
8
Photonics Pod
Electronics Pod
2
A
A
A
A
Power Pod
PCS
Oil filled
Optical
system
A
8
4
16
4
2x2
2
2
O
3
Serial link RS232
2x3
2 Serial link RS232
Tower Base

## Slide 27
Junction Box
SUBMARINE
NODE
10 kW
10 kV / 375 V
8 f.o.
HYBRID MANIFOLD
JUNCTION BOX
E-O
E-O
E-O
E-O
E-O
E-O
O
E
O
E
10 m
10 m
10 m
10 m
10 m
10 m
10 m
O
E
100 m
E
10 m
10 m
POWER POD
100 m
ELECTRICAL MANIFOLD
OPTICAL MANIFOLD
E
10 m
E
10 m
E
10 m
E
10 m
10 m
10 m
O
O
10 m
10 m
O
O
1
2
7
8
1
2
7
8
. . .
. . .
10 m
O
O
ELECTRONICS POD
POWER POD
PHOTONICS POD
E

## Slide 28
375 V
S 8
S 1
375 V INPUT
from MVC
V
PSS
375V / LV
S 9
S 10
PSS
PSS
mC + ADC
FCM
2X8
2
2
2
2
V
T
P
H2O
H2O
H2O
8
Photonics Pod
Electronics Pod
2
A
A
A
A
Power Pod
PCS
16
2
Oil filled
1
ELECTRICAL MANIFOLD
Optical
system
E
8
O
O
1
8
E
E
OPTICAL MANIFOLD
A
O
OPTICAL
FIBERS
3
Serial link RS232
2x3
2 Serial link RS232
8
4
16
2
2
2x2
2
2
4
4
2
2
Junction Box

## Slide 29
NEMO Phase 2 floor electronics 1/2
Fiber optic interface (DWDM transceiver)
Hardware Glink transceiver at 800Mbps
Xilinx Spartan 6 FPGA
Freescale DSP
FEM Interface (proprietary protocol)
Acoustic Interface (AES3 standard protocol)
Slow Control Interface (SPI standard protocol)
Time calibration Interface (proprietary protocol)
Safe reconfiguration from remote
Power requirements ~7.5 W
FCM
Continuous signal sampling:
  192 kHz 24bit-ADC
  2 channels 6Mbps each
Digital Interface Transmitter:
  AES-3 compliant
  Fixed latency
Power requirement: 0.16A @ 5V
AcouDAQ

## Slide 30
NEMO Phase 2 floor electronics 2/2
CPS
SPI interface to FCM
External instruments interface:
  8 insulated serial ports
  Switchable power supply
  Current measure
Temperature and Humidity sensors
Conversion of the DC supply from 375 V to 12 V, 5.5 V, and 4.2 V
Communication via RS485
On/off switching of the power feeding lines
Monitoring of electrical parameters at each feeding power line
Temperature measurment, 3-axis accelerometer and magnetic sensor
SCI
TimCTRL
Communication with the FCM (clock, data and synch. trigger)
Control of the TIM-CAL operations
Propagation of the trigger signal to the TIM-CALs

## Slide 31
Xilinx Spartan 3 FPGA
Freescale DSP
Analog conditioning:
  Non-linear analog compressor (temperature dependent)
ADCs pedestal adjustment
Signal sampling:
  two 100 MHz 8bit-ADCs
  Zero-skipping digital compression
PMT HV management
Temperature & Humidity sensor
Power requirement: 0.4A @ 5V
Safe reconfiguration from remote
Serial port, I2C
NEMO Phase 2 Tower optical module electronics
FEM
Generation of light pulses for calibration (triggered by FEM)
Communication via I2C with FEM
Adjustable pulse level
Pulses reach other floors
TIM-CAL
nanoBeacon
Generation of light pulses for time calibration (triggered by TimCTRL)
Communication via I2C with FEM
Adjustable pulse level

## Slide 32
MEOC
1
2
3
375 VDC + 3 optical fibers
375 VDC + 3 optical fibers
375 VDC + 2 optical fibers
CTA
Splitter
DC/DC
MVC
Anode

## Slide 33: Jitter measurement
Board | JitterRMS [ps]
Generator | 13
PLL | 7.2
FantimeV1 | 8.2
eFcm | 10
FCM | 15
Gen
13 ps
PLL
7.2 ps
FanT
8.2 ps
FCM
15 ps
eFcm
10 ps

## Slide 34: Link budget
38dB for a BER of 10^-12 at 800Mb/s
8.65dB margin without the raman amplifier

## Slide 35
Optical Module in NEMO Phase-2
A glass sphere 13” (Vitrovex):
Single large area photomultiplier : Hamamatsu 10” PMT R7081
Optical gel : Waker SilGel 612
μ-metal wire cage
PMT base circuit : ISEG PHQ7081-i-2m modified
FEM (Front End Module) electronic board
System for timing calibration (TIM-CAL)
13” OM sketch: lateral view
TIM-CAL
FEM
ISEG

## Slide 36
Towards an 8 towers apparatus
14 + 1 floors per tower
6 Optical Modules per floor
120 Floors
672 Optical Modules
Integration
Minimization of cost
Minimization of power consumption
Simplification
~10 years of R&D and
technical progress

## Slide 37
PMT DAQ Boards
PMT DAQ Boards
Hydrophones DAQ Board
GPS receiver
Ethernet Floor Control Module
Floor Control Module
On-Shore
Off-Shore
Slow Control Interface
Floor electronics from onshore to offshore
To other floors
Timing distribution board

## Slide 40
FEM
FCM
PMT If
Tcal If
SFP
Hydro
Om0
Om1
Instr
Bussola
PSS
DC-DC
400  5
3 Twisted Pairs
Z = 100 Ohm
2 Power Wires
2 Twisted Pairs
Z= 100 Ohm
LED
2 x RS232 Port
FPGA
Om2
Om3
2 Fibers
T&H
Om4
Power Supplies
1.2, 1.2, 3.3, 5, 12
Om5

## Slide 41
FPGA
OM #2
T & H Sensor
SFP Laser
SPI Flash
I2C
SPI
RS232
OM #3
OM #1
OM #0
OM #5
OM #4
RS232 Port
Compass (+3.3V)
RS232 Port
Ext Instrument
(Isolated, +12V)
Digital Hydros If
(AES3 compliant)
XADC
Analog Monitor
HS Link
Power Connector
1.2, 1.2, 3.3, 5, 12
(V & I Measurement)
Clock
RS485
RS232
Power + RS232
RS232 Port
Debug
(Isolated, +12V)

## Slide 42
Spartan-6 LX
Trasformatore Wurth 749020010
AD4149 14bit/200MHz
H/T Sensor
Sensirion SHT21
LED Beacon Driver
24V Step Up
Trigger
AFE
DC/DC Power Supply
(TI LMZ10501)
Serial Port(s)
I2C
RS232
LVDS 3 pairs
Clk, Din, Dout
DDR LVDS
Micron N25Q032
Flash
I2C
SPI
1.2V
1.8V
2.5V
3.3V
SPI
5V
16bit DAC
16bit ADC
HV Pmt Control
uBlaze
SPI
RS
FOX924B-10MHz
TE PolyZen
16bit DAC
16bit ADC
AFE Control
& Monitor

## Slide 43
ADC 200 Msps / 14 bit
TI AD4149
T&H Sensor (I2C)
SHT21
LEDPULSER
Controler (I2C)
Step-down DC/DC
5V Input
1.2, 1.8, 2.5, 3.3 Outputs
Analog Front-End
Control (I2C)
FPGA
Xilinx Spartan 6
Analog Front-End
LPF
Passivo, lineare
Current Sensor
Current Sensor

## Slide 44
Serial Port (3.3V)
USER CONN
(Power, AIN, GPIO, I2C, RS232, ...)
FCM CONN
(Power, Data, Clock)
LED Pulser
(TRIG, HV)
Clock Out
GATE In
PMT In
HVPSU CONN
(Power, Control, Monitor)